## Slide 1: The State of IPv6
Geoff Huston APNIC

## Slide 2
The mainstream telecommunications industry has a rich history

## Slide 3
The mainstream telecommunications industry has a rich history
…of making very poor
technology choices

## Slide 4
The mainstream telecommunications industry has a rich history
…of making very poor
technology guesses
and regularly being
taken by
surprise!

## Slide 5: The Internet...
Has been a runaway success that has transformed not just the telecommunications sector, but entire social structures are being altered by the Internet
And now just as we are gearing up, we are about to stuff it up! We’ve used up most of the Internet’s 32bit address pool and that’s a huge problem!

## Slide 6: The Internet...
Has been a runaway success that has transformed not just the telecommunications sector, but entire social structures are being altered by the Internet
And now just as we are gearing up, we are about to stuff it up! We’ve used up most of the Internet’s 32bit address pool and that’s a huge problem!
This is should not be news – we’ve known about
this looming IPocalypse for the past twenty years ...

## Slide 7: IETF Meeting – August 1990

## Slide 8: IETF Meeting – August 1990

## Slide 9: What did we do back in 1992?
We bought some time by removing the CLASS A, B, C address structure from IP addresses

## Slide 10: The CIDR Fix
NSFNET
A&R networks
CIDR
Class-full

## Slide 11: What else did we do back in 1992?
And we started working on a new Internet Protocol – to become IPv6 - to replace IPv4
We left the task of transition until after we had figured out what this new protocol would look like

## Slide 12: zzzzzz
For a while this did not look to be an urgent problem...

## Slide 13: CIDR worked!
NSFNET
A&R networks
CIDR
Class-full

## Slide 14: Meanwhile, we continued to build (IPv4) networks
NSFNET
A&R networks
CIDR
Boom & Bust
Broadband
Mobiles

## Slide 15: The rude awakening
Until all of a sudden the IPv4 address piggy bank was looking extremely empty...

## Slide 16: IPv4 Address Allocations
NSFNET
A&R networks
CIDR
Boom & Bust
Exhaustion!
Broadband
Mobiles

## Slide 17
Ooops!

## Slide 19: The rude awakening
Until all of a sudden the IPv4 address piggy bank was looking extremely empty...
And transition to IPv6 is suddenly a very important topic!

## Slide 20
So, how are we going with the IPv4 to IPv6 transition?

## Slide 21
Do we really need to worry about this?

## Slide 22
Do we really need to worry about this?
Surely IPv6 will just happen – its just a matter
of waiting for the pressure of Ipv4 address
exhaustion to get to sufficient levels of intensity.

## Slide 23
Do we really need to worry about this?
Surely IPv6 will just happen – its just a matter
of waiting for the pressure of Ipv4 address
exhaustion to get to sufficient levels of intensity.
Or maybe not – let’s look a bit closer at the situation ...

## Slide 24
The “inevitability” of technological evolution

## Slide 26
The “inevitability” of technological evolution

## Slide 27
The “inevitability” of technological evolution

## Slide 29
The “inevitability” of technological evolution
Each time we shifted the technology base of the network, the cost efficiencies of the “new” technology in effect motivated the shift from the older technology to the new

## Slide 30
The “inevitability” of technological evolution: Its just economics!

## Slide 31
The “inevitability” of technological evolution
Now lets look at something a little more topical to today!

## Slide 32
The “inevitability” of technological evolution?

## Slide 33
The “inevitability” of technological evolution?

## Slide 34
The challenge often lies in managing the transition from one technology to another

## Slide 35
Option 1: Flag Day!
We all agree to turn off IPv4 and turn on IPv6 EVERYWHERE
All at the same time! All over the Internet!

## Slide 36
Option 1: Flag Day!
We all agree to turn off IPv4 and turn on IPv6 EVERYWHERE
All at the same time! All over the Internet!
We’re just too big!

## Slide 37
Option 2: Parallel Transition!
We start to slide in IPv6 in parallel with IPv4
Then we gradually phase out IPv4

## Slide 38
For this to work we have to start early and finish BEFORE IPv4 address pool exhaustion
IPv6 Deployment
Time
IPv6 Transition – Dual Stack
IPv4 Pool Size
Size of the Internet
Option 2: Parallel Transition!

## Slide 39
Option 2: Parallel Transition!
We start to slide in IPv6 in parallel with Ipv4
Then we gradually phase out IPv6
We’re just too late!
The small print: It’s incredibly difficult for markets to plan without clear price signals, and we never managed to price future scarcity into the Internet model. Our chosen address distribution model was one that deliberately avoided any form of price-based market signaling. We sort of hoped that operators would price future risk. We were very wrong!

## Slide 40
Hybrid IPv4
The increasing scarcity of IPv4 will force carriage providers to add address sharing mechanisms into the IPv4 network
+CGNs
+ALGs
IPv4

## Slide 41
To get from “here” to “there” requires an excursion through an environment of CGNs, CDNs, ALGs and similar middleware ‘solutions’ to IPv4 address exhaustion
IPv4
IPv6
CGNs
ALGs
CDNs
Option 3: Hybrid Transition

## Slide 42
IPv4
IPv6
CGNs
ALGs
CDNs
Transition requires the network owner to undertake capital investment in network service infrastructure to support IPv4 address sharing/rationing.
But will this be merely a temporary phase of transition?

## Slide 43
IPv4
IPv6
CGNs
ALGs
CDNs
Transition requires the network owner to undertake capital investment in network service infrastructure to support IPv4 address sharing/rationing.
What lengths will the network owner then go to to protect the value of this additional investment by locking itself into this “transitional” service model for an extended/indefinite period?
But will this be merely a temporary phase of transition?

## Slide 44
The risk in this transition phase is that the Internet carriage provider heads off in a completely different direction!
IPv4
IPv6
CGNs
ALGs
CDNs
The challenge often lies in managing the transition from one technology to another

## Slide 45: The problem is...
We now need to fuel an ever-expanding Internet:
  without any feed of more IPv4 addresses
and
  without sufficient IPv6 deployment to cut over

## Slide 46: Coping with Demand
Global IPv4 supply shortfall is predicted to reach 800m addresses by 2014

## Slide 47: And it’s not getting any easier...
The metrics of IPv6 deployment could be a lot higher than they are today..

## Slide 48: IPv6 capability, as seen by Google
http://www.google.com/intl/en/ipv6/statistics/
In November2012 only 0.9% of users’ access to Google’s dual stack
services used IPv6

## Slide 49: Where is it?
http://labs.apnic.net/index.shtml
% of users preferring IPv6 – per country

## Slide 50: Relatively, where is it?
Internet
Average

## Slide 51: Absolutely, where is it?

## Slide 52: United States

## Slide 53: France

## Slide 54: China

## Slide 55: Netherlands

## Slide 56: Counting IPv6...
Some 50% of the Internet’s transit ISPs support IPv6 transit
Some 50% of the Internet’s host devices have an active IPv6 stack
  and the rest run Windows XP!
But only 1% of the Internet actually uses IPv6!
  and the problem appears to lie in the last mile access infrastructure!

## Slide 57: What’s gone wrong?
It seems that we’ve managed to achieve only 2 out of 3 necessary prerequisites for IPv6 deployment
To support further growth the access industry has to secure more Ipv4 addresses, deploy (and fund) IPv4 address extension mechanisms, in addition to funding an IPv6 deployment program

## Slide 58: What’s gone wrong?
It seems that we’ve managed to achieve only 2 out of 3 necessary prerequisites for IPv6 deployment
To support further growth the access industry has to purchase Ipv4 addresses, deploy (and fund) IPv4 address extension mechanisms, in addition to funding an IPv6 deployment program
  Why didn’t we do this a few years ago when it would’ve been far easier to undertake this transition?

## Slide 59: Economics!

## Slide 60: Economics!
The Internet’s last mile access is mired in commodity utility economics. Relentless competition has resulted in a sector where margins are thin. A move to IPv6 represents expenditure without immediate revenue gain. This is classic case of economic dislocation in an unbundled industry, where expenditure in one sector:
-carriage- yields benefits in another sector: -content-

## Slide 61: This situation represents a period of considerable uncertainty for our industry

## Slide 62: This situation represents a period of considerable uncertainty for our industry
How long will this transition take?
If I wait will equipment get cheaper or will the user experience get worse?
If we deploy CGNs to keep
IPv4 running, then how long should we plan to keep them in service?
How big should these CGNs be?
Should all users be shunted through a CGN?
What is going to break?
Is Ipv6 really ready for prime time yet?
Will turning on
IPv6 increase my helpdesk call rate?
How much is all this
going to cost?
Can I afford it? Will my revenue base sustain this additional cost?

## Slide 63: Where is this heading?

## Slide 64: In the next five years...
we have a choice

## Slide 65: In the next five years...
Everything gets squashed into HTTP, IPv4 and CGNs
IPv6

## Slide 66: So we need to chose carefully!
We need to think about how to build a post-PC world where content, computation, storage and communications are sustainable abundant and openly available commodities.

## Slide 67: And its not yet clear which path the Internet will take!

## Slide 68: And its not yet clear which path the Internet will take!
market forces

## Slide 69
  If IPv6 is what we are after as an open and accessible platform for further network growth and innovation then the public interest in a continuing open and accessible network needs to be expressed within the dynamics of market pressures.
  Today’s question is:
  How can we do this?

## Slide 70
How can we “manage” this transition?
To ensure that the industry maintains a collective focus on IPv6 as the objective of this exercise!

## Slide 71
How can we “manage” this transition?
To ensure that the industry maintains a collective focus on IPv6 as the objective of this exercise!
And to ensure that we do not get distracted by attempting to optimize what were intended to be temporary measures

## Slide 72: How can we help the Internet through this transition?
Or at least, how can we avoid making it any worse than it is now?

## Slide 74
Yes, that was intentionally left blank!
I really don’t know what will work.
And as far as I can see, nor does anyone else!

## Slide 75
But even though I don’t have an answer here, I have some thoughts to offer about this issue of pulling the Internet though this transition

## Slide 76: Three thoughts...
!
!
!

## Slide 77: Firstly
If we want one working Internet at the end of all this, then keep an eye on the larger picture
  Think about what is our common interest here
  and try to find ways for local interests to converge with our common interest in a single cohesive network that remains open, neutral, and accessible

## Slide 78: Secondly
Addresses should be used in working networks, not hoarded
  Scarcity generates pain and uncertainty
  Hoarding exacerbates scarcity in both its intensity and duration
  Extended scarcity prolongs the pain and increases the unpredictability of the entire transition process
  Closed or opaque address markets create asymmetric information that encourages speculation and hoarding, further exacerbating the problem

## Slide 79: Finally...
Bring it on! A rapid onset of exhaustion and a rapid transition represents the best chance of achieving an IPv6 network as an outcome
  The more time we spend investing time, money and effort in deploying IPv4 address extension mechanisms, the greater the pain to our customers, and the higher the risk that we will lose track of the intended temporary nature of transition and the greater the chances that we will forget about IPv6 as the objective!
  The risk here is no less than the future of open networking and open content - if we get this wrong we will recreate the old stifling vertically bundled carriage monopolies of the telephone era!
  And at that point we’ve lost everything!

## Slide 81: Thank You!